## Slide 1: The Low Frequency (LF) instrument of the Payload for Ultrahigh Energy Observation (PUEO)
Yuchieh Ku
ISCRA 2026
Erice, Italy

## Slide 2: PUEO
35 km
O(Mkm2) of ice
PUEO is a NASA balloon-borne radio detector looking for UHE neutrinos using Antarctic ice

## Slide 3: PUEO
35 km
O(Mkm2) of ice
PUEO is a NASA balloon-borne radio detector looking for UHE neutrinos using Antarctic ice

## Slide 4: PUEO’s science channel - Askaryan
θ=56°

## Slide 5: PUEO’s science channel - Extensive air shower
θ=1.4°
CR
CR

## Slide 6: PUEO/ANITA’s science channel - EAS
𝝉
𝝂𝝉
CC interaction
decay
CR
CR

## Slide 7: Payload for Ultrahigh Energy Observation
Main Instrument (MI): 96 Horn antennas operating at 300-1200 MHz
LowFreq Instrument (LF) : 8 sinuous antennas operating at 50-500 MHz
MI
LF

## Slide 8: Why LF?
LF
MI
A. Cummings
Air shower channel is LowFreq dominant
Cross validation/extend spectra for Askaryan channel
Independently measure
1.Polarization
2.Polarity (+/-)
3.Direction
LF
MI
Notes: Maybe add another slide about Tau channel

## Slide 9: LF Sinuous Antenna
Log-periodic "Sinuous" antenna operates at 50-500 MHz.
Nickel-Copper-Silver fabric sewn on polyester
Dual polarized, independent Horizontal/Vertical polarization
H port
H port
V port
V port
Rp
Rp

## Slide 10: LF Antenna Design and Measurements
Identical back and front lobes.
4-6 dBi gain at boresight.
60°+ 60° antenna beam width.
Applied Research lab anechoic chamber at Warminster, PA
Top view
front
back

## Slide 11: Deployment
backup

## Slide 12: Deployment & performance of LF
Jolt seen in Nav system
Ground Calibration pulser event seen in both MI and LF
Notes: Explain MI and LF rows better
map

## Slide 13: LF pointing resolution
Uncalibrated
After Position Calibration
Preliminary
0.8° resolution in elevation
2.8 °resolution in azimuth

## Slide 14: Galactic noise in LF
(θGC,ɸGC)
Ant boresight (θAnt,ɸAnt)
Payload spinning
Noise power is correlated with antenna orientation relative to the Galactic center (GC).
During the flight, the Sun remained within ~10° of the Galactic Center, making the two contributions difficult to separate. However, during the quiet sun periods (no solar burst) galactic emission is expected to be 1-2 orders of magnitude brighter.
Galactic noise provides a stable reference and will be used to calibrate the LF instrument.
*Band pass to 50-300 MHz
Notes: Sun vs galaxy. stacked map

## Slide 15: Solar radio bursts in LF
HUMAIN observatory
e-Callisto International Network reported ~130 solar radio bursts coincident with PUEO’s flight.
O(10,000) unbiased events (triggered on GPS second) in PUEO’s LF are associated with solar bursts and reconstruct back to sun location
LF spectrogram

## Slide 16: Solar radio bursts in LF

## Slide 17: Summary
LF completed a successful 23 day 10 hour flight with PUEO!
LF will independently quantify signal properties, aiding PUEO in categorizing backgrounds for neutrino searches.
LF is in particular sensitive to EAS signals.
Position calibration of the LF antennas has been performed.
LF noise is dominated by galactic emission < 200 MHz, providing a calibration source.
LF observes events consistent with solar radio bursts, demonstrating how LF expands the science reach of PUEO.

## Slide 18
Back ups

## Slide 19: Science of LF: taus & reflected-CRs
Preliminary
LF increases PUEO’s effective area to the CRs and taus.
A thousand reflected CR events are expected in PUEO’s flight. With information from both MI and the LF.
A. Cummings
Preliminary
*Blue curve is what we flew in PUEO, red are with the LF trg (PUEO II)

## Slide 20: LF Antenna position calibration
For comparison purpose, a translation on X-Y plane is applied to center the LF.
*X,Y,Z directions are align with payload coor, but origin is not
 | 502 | 506 | 606 | 610 | 714 | 814 | 818 | 822
Δr (cm) | -4.8 | -4.7 | -3.4 | -5.3 | -3.7 | -2.7 | -6.5 | -2.6
Δφ(°) | 3.09 | 0.86 | -0.94 | 0.55 | 0.22 | -1.76 | 5.77 | 6.05
Δz(cm) | 0 | -8.5 | 2.1 | -2.8 | -8.2 | -13.7 | -29.8 | -5.7
ΔCable delay (ns) | 0 | 0.05 | 0.43 | -0.04 | -0.09 | 1.03 | 1.10 | 1.05
Calibration performed by varying antenna positions to minimize the difference between expected and measured time delays for antenna pairs.
~22,000 ground calibration events from Taylor Dome VPol were used over a 5–6 hour period.
Design geometry
Preliminary
Preliminary
Calibration uncertainties from MC study: r ~ 1 cm, ϕ ~ 0.5 °, z ~ 5 cm
Notes: Error bar

## Slide 21: LF Antenna Design and Measurements
Impulse response measurements match well with simulations.
Angular responses have consistent phase response, making the coherent sum over antenna pointing at different directions feasible.

## Slide 22: From 1 to 8: LF array Layout
4 layers of hexagon ring provide vertical and horizontal baselines for interferometry.
Keep antennas from blocking each other.
Sub-deg angular resolution with SNR>5

## Slide 23: LF gondola
Carbon fiber tubes
Connectors station
24 ft tall, 12 ft wide
100 lbs in total

## Slide 24: Antenna Wind Loading / Thermal
Thermal study suggests that a >0.1 mm polyester heat shield is necessary.
Wind study suggests that maximum deflection ~6 mm
U = 20m/s
Pressure at center of panel w/out holes
Pressure at center of panel w/ holes
Pmax ~ 0.2 Pa in both cases

## Slide 25: Antenna position calibration
Measurement path:
Δtmeasure through correlate the measured waveforms
Geometry path: Δtexpect (Δ⍴, Δz, Δφ, ΔCabledelay) through known pulser loc, payload loc, and assumed antenna position.
ΔT = Δtmeasure - Δtexpect (Δr, Δz, Δφ, ΔCabledelay)
Minimize

## Slide 26: Calibration uncertainty in MC
CableDelay~0.03ns ⍴~0.9cm φ ~ 0.4 deg z ~ 4.5cm
SNR10
SNR5

## Slide 27: In each LF phi sector
LF Φ I
LF Φ II
LF Φ III
LF Φ I
LF Φ II
LF Φ III
Azimuth in payload coordinate (deg)
To investigate:
Azimuthal (ɸ) has an opposite-signed offset at ɸ and ɸ+180 deg

## Slide 28: Pointing vs SNR

## Slide 29: Galactic noise in LF
(θGC,ɸGC)
Ant boresight (θAnt,ɸAnt)
Payload spinning
Noise power strongly depends on the antennas orientation relative to the GC
Sun is always close (~10 deg) to the GC during the flight, so it’s hard to decouple the effects. However, during the quiet sun periods (no solar burst) galaxy is expected to be 1-2 orders of magnitude brighter.

## Slide 30: Galactic noise in simulation
x
“Power at antennas’ feed”
Haslam sky model
Antenna model
Antenna Temperature
100 MHz

## Slide 31: How to deploy the LF ?

## Slide 32: How to deploy the LF ?

## Slide 33: How to deploy the LF ?

## Slide 34: How to deploy the LF ?

## Slide 35: How to deploy the LF ?

## Slide 36: How to deploy the LF ?

## Slide 37: How to deploy the LF ?

## Slide 38: How to deploy the LF ?

## Slide 39: How to deploy the LF ?

## Slide 40: How to deploy the LF ?
back