## Slide 1: Velocity and Track Reconstruction using HELIX RICH
Duncan Fuehne, University of Chicago
International School of Cosmic Ray Astrophysics
4 August, 2026
Erice, Sicily

## Slide 2: Cosmic Ray Transport Measurements
Galactic cosmic rays (CRs) inform us about the intergalactic medium

## Slide 3: Cosmic Ray Transport Measurements
Galactic cosmic rays (CRs) inform us about the intergalactic medium
Measuring ratio of Primaries to Secondaries probes grammage traversed in galaxy [mass/

## Slide 4: Cosmic Ray Transport Measurements
Galactic cosmic rays (CRs) inform us about the intergalactic medium
Measuring ratio of Primaries to Secondaries probes grammage traversed in galaxy [mass/
Measuring ratio of “clock” isotopes probes confinement time in galaxy

## Slide 5: Be-10 “Clock Isotope”
I. Moskalenko - “AMS02 Days”
Higher energies probe larger region of galaxy
  Relativistic effects
*Only mass resolved measurements shown

## Slide 6: Be-10 “Clock Isotope”
I. Moskalenko - “AMS02 Days”
Higher energies probe larger region of galaxy
  Relativistic effects
HELIX: measure Be-10/Be-9 precisely up to 10 GeV/n
*Only mass resolved measurements shown

## Slide 7: HELIX Overview
Balloon program designed to measure cosmic ray isotopes
1 Engineering flight so far
  Launched 28, 2024 in Kiruna, Sweden
  6 flight
  Successful recovery
  120 million triggers

## Slide 8: HELIX Overview
Balloon program designed to measure cosmic ray isotopes
1 Engineering flight so far
  Launched 28 May, 2024 in Kiruna, Sweden
  6 day flight
  120 million triggers
  Successful recover triggers

## Slide 9: HELIX Overview
Balloon program designed to measure cosmic ray isotopes
1 Engineering flight so far
  Launched 28 May, 2024 in Kiruna, Sweden
  6 day flight
  120 million triggers
  Successful recovery

## Slide 10: HELIX Overview
1st Helix flight payload:
  Built for a mass resolution < 2.5% for Be nuclei < 3 GeV/n
3 Instruments:
  DCT
  TOF
  RICH
Monte Carlo

## Slide 11: HELIX Overview
Drift Chamber Tracker
  Twin-Coil 1 T superconducting magnetic field (
  3 Columns of 72 sense wires to track particles’ trajectories
  Measures CRs’ rigidity
Be Candidate

## Slide 12: Helix Overview
3 Time-Of-Flight (TOF) scintillator paddles
  Top, bottom, bore
  <100 ps timing resolution can measure CR speed (
  Elemental charge separation
Hopefully you saw Minya’s poster regarding TOF reconstruction!
Prelim. Flight TOF Data

## Slide 13: HELIX Overview
Ring Imaging Cherenkov (RICH) detector
  Aerogel radiator (n~1.15)
  12,800 6x6mm Silicon Photo-Multiplier (SiPM) pixels on focal plane
  Above Cherenkov threshold (~1 GeV/n), measures Cherenkov angle (
Be Candidate after kernel density filtering

## Slide 14: RICH Reconstruction
RICH Focal Plane Consists of SiPM hits:

## Slide 15: RICH Reconstruction
RICH Focal Plane Consists of SiPM hits:
Convert using
Ypsilantis-Seguinot
Ypsilantis, Thomas, and Jacques Séguinot. "Theory of ring imaging Cherenkov counters." Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment 343.1 (1994): 30-51.
is Cherenkov angle required for photon to hit pixel

## Slide 16: RICH Reconstruction
RICH Focal Plane Consists of SiPM hits:
Convert using
Ypsilantis-Seguinot methods
  Requires knowing particle's at radiator
  Provided by tracker
  DCT designed for precision tracking only in one plane ( )
Ypsilantis, Thomas, and Jacques Séguinot. "Theory of ring imaging Cherenkov counters." Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment 343.1 (1994): 30-51.
is Cherenkov angle required for photon to hit pixel

## Slide 17: RICH as a Tracker
New technique: use RICH data to assist in tracking!
Use a combined likelihood:
  Custom RICH likelihood
  Track likelihood
    defines relative weight
      =0.95 is optimal
      Tested with Geant4
  Minimize w.r.t. and

## Slide 18: RICH as a Tracker
New technique: use RICH data to assist in tracking!
Use a combined likelihood:
  Custom RICH likelihood
  Track likelihood
    defines relative weight
      =0.95 is optimal
      Tested with Geant4
  Minimize w.r.t. and
Be Likelihood from Geant4
Gaus + background

## Slide 19: RICH as a Tracker
New technique: use RICH data to assist in tracking!
Use a combined likelihood:
  Custom RICH likelihood
  Track likelihood
    defines relative weight
      =0.95 is optimal
      Tested with Geant4
  Minimize w.r.t. and
Be Likelihood from Geant4
Gaus + background

## Slide 20: RICH as a Tracker
New technique: use RICH data to assist in tracking!
Use a combined likelihood:
  Custom RICH likelihood
  Track likelihood
    defines relative weight
      =0.95 is optimal
      Tested with Geant4
  Minimize w.r.t. and
Be Likelihood from Geant4
Gaus + background

## Slide 21: RICH as a Tracker
New technique: use RICH data to assist in tracking!
Use a combined likelihood:
  Custom RICH likelihood
  Track likelihood
    defines relative weight
      =0.95 is optimal
      Tested with Geant4
  Minimize -w.r.t. and
Be Likelihood from Geant4
Gaus + background

## Slide 22: Track-RICH Minimization (TRM) Performance
  Tested on flight data with Binary Random Filter
    Split pixels into two pseudo-random groups
    Reconstruct independently for each group ( and )
w/ TRM
w/ TRM
w/o TRM
w/o TRM

## Slide 23: Track-RICH Minimization (TRM) Performance
  Use residuals from direct ionization hits in Focal Plane to compare tracking performance
  All Z > 3
w/ TRM
w/ TRM
w/o TRM
w/o TRM
Non-bending
Non-bending
Bending
Bending

## Slide 24: Track-RICH Minimization (TRM) Performance
  Use residuals from direct ionization hits in focal plane to compare tracking performance
  All Z > 3
  TRM improves both reconstruction and tracking!
w/ TRM
w/ TRM
w/o TRM
w/o TRM
Non-bending
Non-bending
Bending
Bending

## Slide 25: Launch Video

## Slide 26: Extras

## Slide 27: RICH as a Tracker
New technique: use RICH data to assist in tracking!
Use a combined likelihood:
  Custom RICH likelihood
RICH Likelihood is a function of and
,
Be Likelihood from Geant4

## Slide 28: RICH as a Tracker
  Track likelihood
(or )
Extrapolated Track
DCT
DCT hits

## Slide 29: Kernel Density Filtering

## Slide 30: AMS-02 Be Distribution
Unpublished
Permanent magnet instead of superconducting
  0.14 T
According to Philipp:
Template fit can add bias to resulting measurements
Derome et al., PoS (ICRC2021) 119